## Slide 1: Power Controller

## Slide 2: Voltage Regulators
Buck-Boost Converter
Buck Converter
Boost Converter

## Slide 3: Buck Converter
LTC3621 17V, 1A Synchronous Step-Down Regulator with 3.5μA Quiescent Current
Wide VIN Range: 2.7V to 17V
Wide VOUT Range: 0.6V to VIN
95% Max Efficiency
Constant Frequency (1MHz/2.25MHz)

## Slide 4: Sizing and selecting for Buck Converter
No. | Subsystem | Voltage | Current
a | Data interpretation, Transmission, and Storage | 5.5 V | 250 mA
b | Charge Controller | 5.5 V | 250 mA
c | Loop Controller | 9 V | 50 mA

## Slide 5: Sizing and selecting for Buck Converter
No. | Subsystem | Voltage | Current
a | Data interpretation, Transmission, and Storage | 5.5 V | 250 mA
b | Charge Controller | 5.5 V | 250 mA
Inductor Selection: For starting point is to choose the ripple current to be %40 of I_out(max). To ensure that the ripple current does not exceed the specified maximum.
Given this, a 14.26µH, we can pick the inductor as 15µH, which would suffice
Notes: Inductor Selection: For starting point is to choose the ripple current to be %40 of I_out(max). To ensure that the ripple current does not exceed the specified maximum.

## Slide 6: Sizing and selecting for Buck Converter
Ripple Current Selection
Feedback resistors Selection:

## Slide 7: Sizing and selecting for Buck Converter
Input Capacitor Selection = 10µF ceramic capacitor
Value
Output Capacitor Selection:
a 22µF ceramic capacitor is selected
Notes: The input capacitance, CIN, is needed to filter the square wave current at the drain of the top power MOSFET. To prevent large voltage transients from occurring, a low Equivalente Series Resistance ESR input capacitor sized for the maximum RMS current should be used. The maximum RMS current is given by

## Slide 8: Sizing and selecting for Buck Converter
No. | Subsystem | Voltage | Current
c | Loop Controller | 9 V | 50 mA
Inductor Selection: For starting point is to choose the ripple current to be %40 of I_out(max). To ensure that the ripple current does not exceed the specified maximum.
Given this, a 63,63µH, we can pick the inductor as 68µH, which would suffice

## Slide 9: Sizing and selecting for Buck Converter
Ripple Current Selection
Feedback resistors Selection:

## Slide 10: Sizing and selecting for Buck Converter
Input Capacitor Selection = 10µF ceramic capacitor
Value
Output Capacitor Selection:
a 22µF ceramic capacitor is selected
Notes: The input capacitance, CIN, is needed to filter the square wave current at the drain of the top power MOSFET. To prevent large voltage transients from occurring, a low Equivalente Series Resistance ESR input capacitor sized for the maximum RMS current should be used. The maximum RMS current is given by

## Slide 11: LTSpice Simulation

## Slide 12: Kicad

## Slide 13: Experiments Result
No. | Subsystem | Expected Voltage | Actual Voltage | Expected current | Actual current
a | Data interpretation, Transmission, and Storage | 5.5 V | 5.34 V | 250 mA | 217.26 mA
b | Charge Controller | 5.5 V | 5.31 | 250 mA | 216.42 mA
c | Loop Controller | 9 V | 9.57 V | 50 mA | 54.49 mA

## Slide 14: Reference
Ltc3621-3621-2.Pdf - Analog Devices, www.analog.com/media/en/technical-documentation/data-sheets/ltc3621-3621-2.pdf. Accessed 23 Mar. 2024.
Ti, www.ti.com/lit/an/slva301/slva301.pdf?ts=1694361856373. Accessed 23 Mar. 2024.